## Slide 1: Scalable Management of Trajectories and Context Model Descriptions
Ralph Lange
Institute of Parallel and Distributed Systems (IPVS) Universität Stuttgart
Collaborative Research Center 627

## Slide 2: Motivation
Context-awareness and context-aware computing
Examples:
  Adapt ring volume to ambient noise
  Navigation of blind persons
 Advancements are closely connected to  miniaturization of sensing, computing,  and communication hardware
… the ability of a mobile user’s applications to discover and react to changes in the environment they are situated in.
“
”
(Schilit and Theimer, 1994)

## Slide 3: Motivation (2)
Proliferation of sensing technologies
  Cameras, satellites, weather stations, WSNs, GPS receivers, RFID readers, smartphones, …
Comprehensive models of physical environment
  Differ in geographic extent, aspect, granularity, dynamism, …
  Variety of commercial and non-commercial providers
    Examples: TeleAtlas, Google, OpenStreetMap, CWOP
 Huge potential for context-aware applications
  Ability to select context information from different providers
  Trend: Millions of context models shared by large number of applications
© OpenStreetMap contributors, © CC BY-SA

## Slide 4: Problem Statement
How to provide efficient access to the immense amounts of distributed dynamic context information
?
1. Formal describing of context models
2. Indexing of context model descriptions
3. Efficient real-time trajectory tracking
4. Distributed indexing of 4. space-partitioned trajectories
MOD
Applications
Discovery service for context models
Large amounts of trajectory data
E.g. 3∙107 GPS records per year
High communication cost
Huge storage consumption
Notes: Aerial photo taken by Ralph Lange.

## Slide 5: Overview
Motivation and problem statement
Efficient real-time trajectory tracking
  Formal problem description
  Related work
  Connection-Preserving Dead Reckoning (CDR)
  Generic Remote Trajectory Simplification (GRTS)
  Evaluation and conclusion
Distributed indexing of space-partitioned trajectories
Summary
Notes: Pocket watch from Microsoft Cliparts.

## Slide 6: Tracking: Formal Problem
Actual trajectory a(t) is function R → Rd
Sensed trajectory s(t) with vertices s1, s2, …, sC
  Attribute si.p denotes position at time si.t
  Differs from a(t) due to δsense and movement during Tsense
Simplified trajectory u(t) with vertices u1, u2, …
u1
s2
s1
u2
u3
ε
Definition: Efficient real-time trajectory tracking
  Goals: Minimize |(u1, u2, …)| and communication cost
  Simplification constraint: | u(t) – a(t) | ≤ ε ∀ t
  Real-time constraint: u(t) is available ∀ t ∈ [s1.t,tC]
s3
Linear movements cause redundant vertices

## Slide 7: Tracking: Related Work
Line simplification algorithms
  E.g. Douglas-Peucker heuristic
 High communication cost,  no real-time behavior
Position tracking protocols
  Best mechanism: Dead Reckoning (DR)
 Linear DR with ½ε allows for trajectory  tracking [Trajcevski et al. 2006]
lO
ε
ε
ε
uj
uj +1=lO
lO
lV
lV
ε
>ε
ε
ε
Notes: Globe from Microsoft Cliparts.

## Slide 8: Tracking: CDR
uj +1=lO
Connection-preserving DR extends linear DR
  Object manages lO, lV, and sensing history S
  Second update condition:
    ∃ si ∈ S with |lOsC(si.t) – si.p| > ε
  New prediction starts at last sensed position
CDRm limits computational cost by |S| ≤ m
  Compression approach to prevent periodic updates
uj
lV
< ε
> ε
< ε
< ε

## Slide 9: Tracking: GRTS
Tracking and simplification are different concerns
Basic approach of Generic Remote Trajectory Simplification
  DR to report latest movement
  Arbitrary line simplification algorithm for past movement
    Computational cost ↔ reduction efficiency
   Tracking and simplification must be synchronized!
≈ε
≈ε
≈ε
u1
u2

## Slide 10: Tracking: GRTS Protocol
Variable part
Stable part
Stable part
S
Sensing history S
Moving object
MOD
DR causes update, simplify history S
Update
Variable part
Predicted part
Predic part
Reduce S …

## Slide 11: Tracking: GRTS k/m Variants
So far, not defined how to reduce S …
GRTSk limits variable part to k line sections
  Unlimited computational costs
   Only of theoretical interest
GRTSm limits |S| to m
  Limits computational costs – essential for real-time behavior
  Adds vertex to u(t) at least every m sensing operations
   Compress S if its size exceeds m
Stable part
Variable part
Predicted pa
Sensing history S

## Slide 12: Tracking: GRTS mc Variant
GRTSmc
  si.δ gives maximum deviation along line section from si-1 to si
  Number of compressed positions should be small (c = 1 or 2)
  With uncompressed positions, si.δ may represent varying δsense
s2 with attributes
p = (48.42°,9.01°)
t = 2009-12-15 14:25:17.3
δ = 7m
|S| = m
DR causes update

## Slide 13: Tracking: GRTS*Sec and GRTS*Opt
GRTS*Opt – with optimal simplification algorithm [Imai and Iri 1988]
  Reduces simplification to shortest-path problem
  Segmentation by k or m influences reduction efficiency
GRTS*Sec – with Section Heuristic [e.g. Meratnia and de By 2004]
  Online algorithm enables per-sense simplification
  Proposed improved version, optimizing |S|

## Slide 14: Tracking: Evaluation Setup
Comparing CDR variants and GRTS* realizations to …
  Linear DR with ½ε (LDRH)
  Optimal offline simplification (RefOpt)
  Douglas-Peucker algorithm (RefDP)
Simulated with real GPS traces from OpenStreetMap
  > 1.2 million sensed positions, i.e. > 330 h of data
  Sensor inaccuracy of δsense = 7.8 m
  Sensing period Tsense = 1 s
  Maximum acceleration amax = 10 m/s²

## Slide 15: Tracking: Reduction Efficiency
Low reduction because simplification is based on dead reckoning
CDR outperforms LDRH by factor two or more. CDRm with m = 500 suffices
GRTS*Sec achieves 85 to 90% of best possible reduction. GRTSmSec with m = 500 suffices
GRTS*Opt achieves up to 97% of best possible reduction. GRTSmcOpt with m = 500 outperforms GRTSkOpt with k = 1
All GRTS realizations outperform offline simplification with RefDP

## Slide 16: Tracking: Communication
LDRH sends twice as many updates because of ½ε
With CDR and GRTS, communication cost slightly increase with reduction efficiency

## Slide 17: Tracking: Computing Time
CDRm limits computational cost effectively
Costs for CDRm and GRTSmSec are comparable
High computational cost for GRTSmcOpt compared to GRTSmSec
GRTSm and GRTSmc may limit computational cost very effectively
2600

## Slide 18: Tracking: Conclusion
LDRH
CDR
GRTS
CDRm
GRTSk
GRTSm
GRTSmc
GRTSmcSec
GRTSmOpt
GRTSkSec
GRTSkOpt
GRTSmSec
GRTSmcOpt
If communication cost have maximum priority
Simple approach, good reduction
Best reduction, high computational costs

## Slide 19: Distributed Indexing of Trajectories
Managing large number of mobile objects requires distributed MOD
  Coordinate-based query: “Which objects were located in R during [t1,t2]?”
  Trajectory-based query: “What distance covered object o2 during [t3,t4]?”
o2
 | Spatial partitioning | Object-based partitioning
Coordinate-based queries |  | –
Trajectory-based queries | ? | 
Update-aware distribution |  | –
o1
o1
o2
s2
s1
s1
s2
How to determine and route to relevant servers efficiently?

## Slide 20: Distributed Indexing of Trajectories (2)
Trajectory-based routing along queried trajectory can take many hops
  Depends on queried time span and trajectory route
Solution: Distributed Trajectory Index (DTI)
  DTI scheme creates independent index (overlay) for each trajectory
  Enables efficient routing by pointers to temporally distant positions
  DTI+S also stores summaries (speed, MBR, …) on segments
  Linear storage consumption
s3
s4
s2
s1
s6
s7
s5
2
0
1
3
ta
4

## Slide 21: Distributed Indexing of Trajectories (3)
DTI+S can reduce processing times by more than 95%, but accounts for less than 2.3% of the overall storage consumption.

## Slide 22: Summary
Proliferation of sensing technologies constitutes huge potential for context-aware applications
  1. CDR and GRTS for real-time trajectory tracking
  2. DTI for scalable distributed indexing of trajectories
  3. Formalism and SDC-Tree for describing and indexing of context models (see thesis)
MOD
Applications
How to provide efficient access to the immense amounts of distributed dynamic context information
?
Notes: Aerial photo taken by Ralph Lange.

## Slide 23: Thank you for your attention!
Selected Publications:
Ralph Lange, Frank Dürr, Kurt Rothermel: “Indexing Source Descriptions based on Defined Classes”. In: Proc. of 14th IDEAS. Montreal, QC, Canada. Aug 2010.
Ralph Lange, Frank Dürr, Kurt Rothermel : “Efficient Tracking of Moving Objects using Generic Remote Trajectory Simplification”. In: Proc. of 8th PerCom Workshops. Mannheim, Germany. Mar 2010.
Ralph Lange, Harald Weinschrott, Lars Geiger, André Blessing, Frank Dürr, Kurt Rothermel, Hinrich Schütze: “On a Generic Uncertainty Model for Position Information”. In: Proc. of 1st QuaCon. Stuttgart, Germany. Jun 2009.
Ralph Lange, Tobias Farrell, Frank Dürr, Kurt Rothermel: “Remote Real-Time Trajectory Simplification”. In: Proc. of 7th PerCom. Galveston, TX, USA. Mar 2009.
Ralph Lange, Frank Dürr, Kurt Rothermel: “Scalable Processing of Trajectory-Based Queries in Space-Partitioned Moving Objects Databases”. In: Proc. of 16th ACM GIS. Irvine, CA, USA. Nov 2008.
Ralph Lange, Frank Dürr, Kurt Rothermel: “Online Trajectory Data Reduction using Connection-preserving Dead Reckoning”. In: Proc. of 5th MobiQuitous. Dublin, Ireland. Jul 2008.
Tobias Farrell, Ralph Lange, Kurt Rothermel: “Energy-efficient Tracking of Mobile Objects with Early Distance-based Reporting”. In: Proc. of 4th MobiQuitous . Philadelphia, PA, USA. Aug 2007.
 See www.lange-ralph.de for complete list